## Slide 1: 8255 PPI

## Slide 2: Features
It is a programmable device.
It has 24 I/O programmable pins like PA,PB,PC (3-8 pins).
TTL compatible.
Improved dc driving capability
PPI – Programmable Peripheral Interface
It is an I/O port chip used for interfacing I/O devices with microprocessor

## Slide 3: Pin Diagram

## Slide 4: Function of pins:
Data bus(D0-D7):These are 8-bit bi-directional buses, connected to 8085 data bus for transferring data.
CS: This is Active Low signal. When it is low, then data is transfer from 8085.
Read: This is Active Low signal, when it is Low read operation will be start.
Write: This is Active Low signal, when it is Low Write operation will be start.

## Slide 5
Address (A0-A1):This is used to select the ports. like this
A1 | A0 | Select
0 | 0 | PA
0 | 1 | PB
1 | 0 | PC
1 | 1 | Control reg.

## Slide 6
RESET: This is used to reset the device. That means clear control registers.
PA0-PA7:It is the 8-bit bi-directional I/O pins used to send the data to peripheral or to receive the data from peripheral.
PB0-PB7:Similar to PA
PC0-PC7:This is also 8-bit bidirectional I/O pins. These lines are divided into two groups.
PC0 to PC3(Lower Groups)
PC4 to PC7 (Higher groups)
These two groups working in separately using 4 data’s.

## Slide 7: Block Diagram

## Slide 8: Data Bus buffer
It is a 8-bit bidirectional Data bus.
Used to interface between 8255 data bus with system bus.
The internal data bus and Outer pins D0-D7 pins are connected in internally.
The direction of data buffer is decided by Read/Control Logic.

## Slide 9: Read/Write Control Logic
This is getting the input signals from control bus and Address bus
Control signal are RD and WR.
Address signals are A0,A1,and CS.
8255 operation is enabled or disabled by CS.

## Slide 10: Group A and Group B control
Group A and B get the Control
Signal from CPU and send the command to the individual control blocks.
Group A send the control signal to port A and Port C (Upper) PC7-PC4.
Group B send the control signal to port B and Port C (Lower) PC3-PC0.
PORT A:
This is a 8-bit buffered I/O latch.
It can be programmed by mode 0 , mode 1, mode 2 .

## Slide 11
PORT B:
This is a 8-bit buffer I/O latch.
It can be programmed by mode 0 and mode 1.
PORT C:
This is a 8-bit Unlatched buffer Input and an Output latch.
It is splitted into two parts.
It can be programmed by bit set/reset operation.

## Slide 12: Operation modes:
BIT SET/RESET MODE:
The PORT C can be Set or Reset by sending OUT instruction to the CONTROL registers.
I/O MODES:
MODE 0(Simple input / Output):
In this mode, ports A, B are used as two simple 8-bit I/O ports
port C as two 4-bit ports.
Each port can be programmed to function as simply an input port or an output port. The input/output features in Mode 0 are as follows.
Features:
Outputs are latched , Inputs are buffered not latched.
Ports do not have Handshake or interrupt capability.

## Slide 13
MODE 1 :(Input/output with Hand shake)
In this mode, handshake signals are exchanged between the MPU and peripherals prior to data transfer.
Features:
1. Two ports (A and B) function as 8-bit I/O ports.
They can be configured as either as input or output ports.
2. Each port uses three lines from ort C as handshake signals.
The remaining two lines of Port C can be used for simple I/O operations.
3. Input and Output data are latched.
4. Interrupt logic is supported.

## Slide 14
Example:
The computer send the data to the printer large speed compared to the printer.
When computer send the data according to the printer speed at the time only, printer can accept.
If printer is not ready to accept the data then after sending the data bus , computer uses another handshaking signal to tell printer that valid data is available on the data bus.
Each port uses three lines from port C as handshake signals
Computer
Printer
DATA BUS
STB
ACK
Busy

## Slide 15
MODE 2:bi-directional I/O data transfer:
This mode allows bidirectional data transfer over a single 8-bit data bus using handshake signals.
This feature is possible only Group A
Port A is working as 8-biy bidirectional.
PC3-PC7 is used for handshaking purpose.
The data is sent by CPU through this port , when the peripheral request it.

## Slide 16
CONTROL WORD FORMATS:
In the INPUT mode , When RESET is High all 24 pins (3-ports) be a input mode.
i.e. all flip flops are cleared and the interrupts are rest.
This condition is maintained even after RESET goes low.
This can be avoid by writing single control word to the control registers , when required.

## Slide 17
FOR BIT SET/RESET MODE:
This is bit set/reset control word format.
X X X
Don’t care
Bit select
B0
B1
B2
D7 | D6 | D5 | D4 | D3 | D2 | D1 | D0
0 | 1 | 2 | 3 | 4 | 5 | 6 | 7
0 | 1 | 0 | 1 | 0 | 1 | 0 | 1
0 | 0 | 1 | 1 | 0 | 0 | 1 | 1
0 | 0 | 0 | 0 | 1 | 1 | 1 | 1
BIT SET/RESET
1=SET
0=RESET
BIT SET/RESET FLAG
=0 Active

## Slide 18
PC0-PC7 is set or reset as per the status of D0.
A BSR word is written for each bit
Example:
PC3 is Set then control register will be 0XXX0111.
PC4 is Reset then control register will be 0XXX01000.
X is a don’t care.

## Slide 19
Ex. 1: Set to 1 bit 4 of Port C |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  | 
 |  | 0 | X | X | X | 1 |  | 0 |  | 0 |  | 1 | = | 09H,… |  | 
PC bit set / reset control word |  |  |  |  |  | Bit 4 of PC |  |  |  |  |  | Set to 1 |  |  |  | 
 |  |  | Don’t cares |  |  |  |  |  |  |  |  |  |  |  |  | 
 |  |  |  |  |  |  |  |  |  |  | Required instructions |  |  |  |  | 
 |  |  |  |  |  |  |  |  |  |  | MOV AL, 09H |  |  |  |  | 
 |  |  |  |  |  |  |  |  |  |  | OUT 7FH, AL |  |  |  |  | 

## Slide 20
Ex. 2: Reset to 0 bit 6 of Port C |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  | 
 |  | 0 | X | X | X | 1 |  | 1 |  | 0 |  | 0 | = | 0CH,… |  | 
PC bit set / reset control word |  |  |  |  |  | Bit 6 of PC |  |  |  |  |  | Reset to 0 |  |  |  | 
 |  |  | Don’t cares |  |  |  |  |  |  |  |  |  |  |  |  | 
 |  |  |  |  |  |  |  |  |  |  | Required instructions |  |  |  |  | 
 |  |  |  |  |  |  |  |  |  |  | MOV AL, 0CH |  |  |  |  | 
 |  |  |  |  |  |  |  |  |  |  | OUT 7FH, AL |  |  |  |  | 

## Slide 21
FOR I/O MODE:
The mode format for I/O as shown in figure
D7 | D6 | D5 | D4 | D3 | D2 | D1 | D0
Group A
Port C Upper 1=Input 0=Output
Port A 1=Input 0=Output
Mode selection 00=Port A in mode 0 01=Port A in mode 1 1x(0/1)=Port A in mode 2
Group B
Port C Lower 1=Input 0=Output
Port B 1=Input 0=Output
Mode selection 0=Port B in mode 0 1=Port B in mode 1
Mode set flag=1=Active. Means mode definition control word

## Slide 22
The control word for both mode is same.
Bit D7 is used for specifying whether word loaded in to Bit set/reset mode or Mode definition word.
D7=1=Mode definition mode.
D7=0=Bit set/Reset mode.

## Slide 23
Ex. 1: Configure Port A as i/p in Mode 0, Port B as o/p in mode 0, Port C (Lower) as o/p and Port C (Upper) as i/p ports. |  |  |  |  |  |  |  |  |  |  |  | 
Required MD control word: |  |  |  |  |  |  |  |  |  |  |  | 
 |  | 1 | 0 | 0 | 1 | 1 | 0 | 0 | 0 | = |  | 98H
MD control |  |  |  |  |  |  |  |  | PC Lower as o/p |  |  | 
 | PA in Mode 0 |  |  |  |  |  |  | PB as o/p Reqd. instrns. |  |  |  | 
 |  | PA as i/p |  |  |  |  | PB in Mode 0 |  |  |  | MOV AL, 98H | 
 |  |  |  |  |  | PC Upper as i/p |  |  |  |  | OUT 7FH, AL | 

## Slide 24
Ex. 2: Configure Port A as i/p in Mode 1, Port B as o/p in mode 1, Port C7-8 as i/p ports. (PC5-0 are handshake lines, some i/p lines and others o/p. So they are shown as X) |  |  |  |  |  |  |  |  |  |  |  |  | 
Required MD control word: |  |  |  |  |  |  |  |  |  |  |  |  | 
 |  | 1 | 0 |  | 1 | 1 | 1 | 1 | 0 | X | = |  | BCH or BDH
MD control |  |  |  |  |  |  |  |  |  | PC3-0 as don’t care |  |  | 
 | PA in Mode 1 |  |  |  |  |  |  |  | PB as o/p Reqd. Instrns. |  |  |  | 
 |  | PA as i/p |  |  |  |  |  | PB in Mode 1 |  |  |  | MOV AL,BCH | 
 |  |  |  |  |  | PC Upper(C7-8) as i/p |  |  |  |  |  | OUT 7FH, AL | 

## Slide 25
Ex. 3:Configure Port A in Mode 2, Port B as o/p in mode 1. (PC5-0 are handshake lines for Port A and PC2-0 are handshake signals for port B) |  |  |  |  |  |  |  |  |  |  |  | 
Required MD control word: |  |  |  |  |  |  |  |  |  |  |  | 
 |  | 1 | 1 | 0 | X | X | 1 | 0 | X | = |  | C4H / C5H..
MD control |  |  |  |  |  |  |  |  | PC3-0 as handshake |  |  | 
 | PA in Mode 2 |  |  |  |  |  |  | PB as o/p Reqd. instrns. |  |  |  | 
 | PA bidirectional |  |  |  |  |  | PB in Mode 1 |  |  |  | MOV AL, C4H | 
 |  |  |  | PC7-0 as handshake |  |  |  |  |  |  | OUT 7FH, AL | 

## Slide 26
Handshake Interrupt i/p port
STB*A (PC4)
Port A
PA7-0
8255
IBFA INT A
(PC5) (PC3)
For Port A as handshake interrupt input port:
INTA is PC3
STB*A is PC4
IBFA is PC5
26

## Slide 27
Handshake Interrupt i/p port
STB*
IBF
INT
RD*
Data
from
I/O dev.
27

## Slide 28
Handshake interrupt i/p port
When i/p device has data to send it checks if IBF (input buffer full) signal is 0.
If 0, it sends data on PB7-0 and activates STB* (Strobe) signal. STB* is active low.
When STB* goes high, the data enters the port and IBF gets activated.
If the Port interrupt is enabled, INT is activated. This interrupts the processor.
Processor reads the port during the ISS. Then IBF and INT get deactivated.
28

## Slide 29
Handshake interrupt o/p port
ACK*B (PC2)
8255
Port B
PB7-0
OBF*B INT B
(PC1) (PC0)
For Port A as handshake interrupt output port:
INTB is PC0
ACK*B is PC2
OBF*B is PC1
29

## Slide 30
Handshake interrupt o/p port
WR*
OBF*
INT
ACK*
Data sent out
on port pins
30

## Slide 31
Handshake interrupt o/p port
When o/p device wants to receive data it checks if OBF* (output buffer full) signal is 0.
If 0, it receives data on PB7-0 and activates ACK* (Acknowledge) signal. ACK* is active low.
When ACK* goes high, the data goes out of the port and OBF* is set to 1.
If the Port interrupt is enabled, INT is activated. This interrupts the processor.
Processor sends another byte to the port during the ISS. Then OBF* and INT are reset to 0.
31

## Slide 32
Handshake Status Check I/O
Interrupt is disabled for the port using PCBSR
Even if new data is entered into I/p buffer by I/O device INT o/p is not going to be activated for i/p operation
How processor knows that the i/p buffer has new data?
Even if I/O device has emptied the o/p buffer, INT o/p is not going to be activated for o/p operation
How the processor knows that the o/p buffer is empty?
Processor reads the status of the port for this purpose
32

## Slide 33
Port C as provider of Status
PC provides status info of PA & PB when not in mode 0
PC7 PC6 PC5 PC4 PC3 PC2 PC1 PC0
OBF*
INTE
IBF
INTE
INT
INTE
IBF/OBF*
INT
PA status in Mode 1 o/p (along with INT)
PA status in Mode 1 i/p
PB status in Mode 1
i/p or o/p
PA status in Mode 2
IBF = i/p buffer full
OBF* = o/p buffer full
INT = Interrupt INTE = Interrupt Enable
33

## Slide 34
Handshake status check i/p port
Suppose Port B is in mode 1 status check i/p Processor reads bit 1 (IBF) of Port C repeatedly till it is set and then the processor reads Port B AGAIN: IN AL, 7EH; Read Port C ROR AL, 1; ROR AL, 1; Check bit 1 of Port C JNC AGAIN; If it is 0, repeat checking IN AL, 7DH ; Read from Port B
34