## Slide 1: PROGRAMMABLE PERIPHERAL INTERFACE -8255
Features:
It is a programmable device.
It has 24 I/O programmable pins like PA,PB,PC (3-8 pins).
T T L compatible.
Improved dc driving capability

## Slide 2: Pin Diagram

## Slide 3: Function of pins:
Data bus(D0-D7):These are 8-bit bi-directional buses, connected to 8085 data bus for transferring data.
CS: This is Active Low signal. When it is low, then data is transfer from 8085.
Read: This is Active Low signal, when it is Low read operation will be start.
Write: This is Active Low signal, when it is Low Write operation will be start.

## Slide 4
Address (A0-A1):This is used to select the ports. like this
A1 | A0 | Select
0 | 0 | PA
0 | 1 | PB
1 | 0 | PC
1 | 1 | Control reg.

## Slide 5
RESET: This is used to reset the device. That means clear control registers.
PA0-PA7:It is the 8-bit bi-directional I/O pins used to send the data to peripheral or
or to receive the data from peripheral.
PB0-PB7:Similar to PA
PC0-PC7:This is also 8-bit bidirectional I/O pins. These lines are divided into two groups.
PC0 to PC3(Lower Groups)
PC4 to PC7 (Higher groups)
These two groups working in separately using 4 data’s.

## Slide 6: Block Diagram

## Slide 7
Data Bus buffer:
It is a 8-bit bidirectional Data bus.
Used to interface between 8255 data bus with system bus.
The internal data bus and Outer pins D0-D7 pins are connected in internally.
The direction of data buffer is decided by Read/Control Logic.

## Slide 8
Read/Write Control Logic:
This is getting the input signals from control bus and Address bus
Control signal are RD and WR.
Address signals are A0,A1,and CS.
8255 operation is enabled or disabled by CS.

## Slide 9
Group A and Group B control:
Group A and B get the Control
Signal from CPU and send the command to the individual control blocks.
Group A send the control signal to port A and Port C (Upper) PC7-PC4.
Group B send the control signal to port B and Port C (Lower) PC3-PC0.
PORT A:
This is a 8-bit buffered I/O latch.
It can be programmed by mode 0 , mode 1, mode 2 .

## Slide 10
PORT B:
This is a 8-bit buffer I/O latch.
It can be programmed by mode 0 and mode 1.
PORT C:
This is a 8-bit Unlatched buffer Input and an Output latch.
It is splitted into two parts.
It can be programmed by bit set/reset operation.

## Slide 11: Operation modes:
BIT SET/RESET MODE:
The PORT C can be Set or Reset by sending OUT instruction to the CONTROL registers.
I/O MODES:
MODE 0(Simple input / Output):
In this mode , port A, port B and port C is used as individually (Simply).
Features:
Outputs are latched , Inputs are buffered not latched.
Ports do not have Handshake or interrupt capability.

## Slide 12
MODE 1 :(Input/output with Hand shake)
In this mode, input or output is transferred by hand shaking Signals.
Handshaking signals is used to transfer data between whose data transfer is not same.
Computer
Printer
DATA BUS
STB
ACK
Busy

## Slide 13
Example:
The computer send the data to the printer large speed compared to the printer.
When computer send the data according to the printer speed at the time only, printer can accept.
If printer is not ready to accept the data then after sending the data bus , computer uses another handshaking signal to tell printer that valid data is available on the data bus.
Each port uses three lines from port C as handshake signals

## Slide 14
MODE 2:bi-directional I/O data transfer:
This mode allows bidirectional data transfer over a single 8-bit data bus using handshake signals.
This feature is possible only Group A
Port A is working as 8-biy bidirectional.
PC3-PC7 is used for handshaking purpose.
The data is sent by CPU through this port , when the peripheral request it.
CONTROL WORD FORMATS:
In the INPUT mode , When RESET is High all 24 pins (3-ports) be a input mode.

## Slide 15
i.e all flip flops are cleared and the interrupts are rest.
This condition is maintained even after RESET goes low.
This can be avoid by writing single control word to the control registers , when required.

## Slide 16
FOR BIT SET/RESET MODE:
This is bit set/reset control word format.
X X X
Don’t care
Bit select
B0
B1
B2
D7 | D6 | D5 | D4 | D3 | D2 | D1 | D0
0 | 1 | 2 | 3 | 4 | 5 | 6 | 7
0 | 1 | 0 | 1 | 0 | 1 | 0 | 1
0 | 0 | 1 | 1 | 0 | 0 | 1 | 1
0 | 0 | 0 | 0 | 1 | 1 | 1 | 1
BIT SET/RESET
1=SET
0=RESET
BIT SET/RESET FLAG
=0 Active

## Slide 17
PC0-PC7 is set or reset as per the status of D0.
A BSR word is written for each bit
Example:
PC3 is Set then control register will be 0XXX0111.
PC4 is Reset then control register will be 0XXX01000.
X is a don’t care.

## Slide 18
FOR I/O MODE:
The mode format for I/O as shown in figure
D7 | D6 | D5 | D4 | D3 | D2 | D1 | D0
Group A
Port C Upper 1=Input 0=Output
Port B 1=Input 0=Output
Mode selection 00=mode 0 01=mode 1 1x=mode 2
Group B
Port C Lower 1=Input 0=Output
Port B 1=Input 0=Output
Mode selection 0=mode 0 1=mode 1
Mode set flag=1=Active

## Slide 19
The control word for both mode is same.
Bit D7 is used for specifying whether word loaded in to Bit set/reset mode or Mode definition word.
D7=1=Mode definition mode.
D7=0=Bit set/Reset mode.

## Slide 20: Thank you
Q&A

## Slide 21: Prepared by Prof.R.K.Kumar